## Slide 1: Control of Large-Scale Motions in Turbulent Boundary Layers
Alex Tsolovikos
PhD Candidate
Supervisors: David Goldstein and Efstathios Bakolas
Department of Aerospace Engineering and Engineering Mechanics
The University of Texas at Austin
Tuesday, August 2nd, 2022

## Slide 2: What is a Large-Scale Motion?
Coherent motions in wall-bounded turbulent flows
Characteristics:
  Size in the order of the boundary layer thickness
  Large fraction of the turbulent kinetic energy
  Significant contribution to average Reynolds shear stresses
Consist of smaller structures (e.g. hairpin vortices)

## Slide 3: Control Scheme
Re-energize the boundary layer by moving LSMs toward the wall

## Slide 4: Turbulent Boundary Layer DNS
Direct numerical simulation of a turbulent boundary layer at Reθ = 1100 - 2000 using the spectral element code Nek5000 | Boundary layer is tripped with random streamwise forcing
Q Criterion isosurfaces colored by height

## Slide 5: A Closer Look at Velocity Fluctuations
Reθ = 1800 | Isosurfaces at u’ = ±0.1Uinf
δ99
Slow
Fast

## Slide 6: Side View of Positive Fluctuations
Positive velocity fluctuations reside lower in the boundary layer
Fast
δ99

## Slide 7: Side View of Negative Fluctuations
Negative velocity fluctuations reside higher in the boundary layer
Slow
δ99

## Slide 8: Model Predictive Control of LSMs
Detect
Volumes of LSMs to target
Predict
LSM Movement
Actuate
Create downwash when LSM is near the actuator

## Slide 9: Detect an LSM
Use the 3D flowfield to directly detect LSMs (e.g. by low-pass filtering the streamwise velocity fluctuations)
Volume can be represented with a Gaussian mixture

## Slide 10: Predict LSM Trajectory
Use Taylor’s hypothesis to predict the trajectory of an LSM

## Slide 11: Creating Downwash
Gaussian Jet
Mid-plane streamwise velocity
45 deg pitch angle

## Slide 12: Force Field Distributions (x-y plane)
Off-the-wall Gaussian Jet
Fx = -Fy
Wall-mounted Gamma Distribution Jet

## Slide 13: Plasma Actuators*
Flow entrainment
Body Forces of a Plasma Actuator
Experiment
Suzen & Huang Model
*Brauner, T., Laizet, S., Benard, N. and Moreau, E., 2016. Modelling of dielectric barrier discharge plasma actuators for direct numerical simulations. In 8th AIAA Flow Control Conference (p. 3774).

## Slide 14: Gaussian Jet: Mid-plane Wall-Normal Velocity

## Slide 15: Gamma Jet: Mid-plane Wall Normal Velocity

## Slide 16: Optimal Output Tracking Control
Maximize Downwash
Minimize Control Effort
Optimal Control Inputs
Jet Magnitude
We need a model for predicting the downwash for a given input

## Slide 17: Optimal Output Tracking Control
Maximize Downwash
Minimize Control Effort
Optimal Control Inputs
Jet Magnitude
We need a model for predicting the downwash for a given input
ROM Dynamics
+
Input Constraints

## Slide 18: Sparsity-Promoting DMD with Control
Tsolovikos et al., Estimation and Control of Fluid Flows Using Sparsity-Promoting Dynamic Mode Decomposition, IEEE Control Systems Letters, 2021
DMDc Reduced-Order Model:
Sparsity-Promoting Optimization:
Use reweighted L1 norm instead

## Slide 19: Control of Fluid Volumes | Laminar Boundary Layer
Tsolovikos et al., Model Predictive Control of Material Volumes with Application to Vortical Structures, AIAA Journal, 2021
Volumes visualized by particles

## Slide 20: Control of Synthetic LSMs | Laminar Boundary Layer

## Slide 21: Control of Synthetic LSMs
Change in Vorticity Fluctuation RMS when targeting a synthetic LSM

## Slide 22: Reduced-Order Models for Downwash Prediction
DNS Ensemble Average
Best POD Projection
DMDc
tlsDMDc
tlsDMDc + GP*
*To be published

## Slide 23: Reinforcement Learning (No Model Needed)
Proximal Policy Optimization with LSTM policy and discrete actions (jet is on/off)

## Slide 24: Next Steps
LSMs in an adverse pressure gradient turbulent boundary layer
MPC control of LSMs for separation delay
Large-eddy simulations to speed up computations
Dynamic Mode Decomposition + Gaussian Processes for more accurate flowfield predictions
Reinforcement learning for LSM control
alextsolovikos.github.io